## Slide 1
B18: PROBTON
ASIC Solution for Optical Probe Station for Photonic Integrated Circuits Packaging and Testing
CHIPATON 2026 TRACK B : CIRCUITS FOR SENSOR
.
TIM LAM • VICTORIA TJHIN • ABRAAR ALAM
BELKACEM BENADDA • NITIN INDUKURI • REZA SETIABEKTI • ASHMITA SAHA
- TEAM MEMBERS -

## Slide 2
INDUSTRY CHALLENGES
Page 2
[1] L. Ranno et al., “Integrated Photonics Packaging: Challenges and Opportunities,” ACS photonics, vol. 9, no. 11, pp. 3467–3485, Oct. 2022, doi: https://doi.org/10.1021/acsphotonics.2c00891.
[2] The Business Research Company, “Silicon Photonics Market Report 2026,” Jan. 2026. Available: https://www.thebusinessresearchcompany.com/report/silicon-photonics-global-market-report
70-80% of photonics costs are from packaging, requiring costly proprietary alignment systems
[1]
[2]

## Slide 3
<μm
precision
<$5k
Open
source
Budget build
Custom setup
VALUE PROPOSITION
Democratize
proprietary alignment
feedback
systems
5.7
steps to align
2
1
3
4

## Slide 4
SETUP

## Slide 5
TEST SETUP

## Slide 6
Link: https://doi.org/10.1016/j.ohx.2022.e00317
Estimated Price: less than $883
Key Specifications:
  Sensitivity: 25.0 nm/V
  Resolution:
  Backlash: 160 – 195 nm
  Step error: ~ 7%
XY-Stage [1]
[3] H.-S. Liao et al., HardwareX, vol. 11, p. e00317, 2022.
[4] W.-M. Wang et al., Nanotechnology, vol. 24, p. 455503, 2013.
INTERFACES
Photodetector
Thorlabs FDSP625 Pigtailed Si Photodiode
Link: https://www.thorlabs.com/thorproduct.cfm?partnumber=FDSP625
Estimated Price: $178.32
Key Specifications:
  Spectral Band: 320 nm to 1000 nm
  Response Speed: 700 ps rise/fall time
  Noise: 0.01 nA dark current
Link:
https://doi.org/10.1088/0957-4484/24/45/455503
Estimated Price: less than $125 (without DAQ)
Key Specifications:
  XY Range: 5 µm
  Nonlinearity: 2.11% X / 2.73% Y
  Noise / Resolution: ~0.06 nm
  Resonance: ~360 Hz (X/Y)
MEMS
Actuator [2]
Buzzer-Scanner (Wang et al. 2013)

## Slide 7
Pin allocation:
Power:
1. Analog
2. Digital
Input:
1. Photocurrent (analog)
2. User instruction config (digital)
Output:
1. Filtered Amp Signal (analog)
2. Area Signal (analog)
3. Analog-time pulse (analog)
4. Offset direction (digital)
5. Normalized Area (digital)
6. Error x (digital)
7. Error y (digital)
8. Global motion x control (digital)
9. Global motion y control (digital)
10. MEMs control (analog)
11. Analog Wave Mixer (analog)
Total pin count: 15

## Slide 8
ANALOG DOMAIN
AFE & MEMS WAVE MIXER

## Slide 9
DIGITAL
DOMAIN

## Slide 10
Three-Point Gaussian Area Method
SIGNAL PROCESSING ALGORITHM
3-Point Sampling Workflow :
  Readout – Boot and sweep
  User config movement and sweep
  Smart movement and sweep
  Iterate until alignment and stop
[5] J. Li, J. D. Valentine, and A. E. Rana, Nucl. Instrum. Methods Phys. Res. A, vol. 422, no. 1–3, pp. 438–443, 1999.

## Slide 11
20K+
SIGNAL PROCESSING ALGORITHM

## Slide 12
20K+
3-POINT SAMPLING WORKFLOW
  Readout – Boot and sweep
  User config movement and sweep
  Smart movement and sweep
  Iterate until alignment and stop

## Slide 13
SIMULATION RESULTS
Active alignment Tracking for Gaussian Peak. (WIth Errors)
Average Convergence Steps to 1% Transmission loss 5.7 ± 1.1
Monte Carlo Simulation

## Slide 14
TIM (TEAM LEAD)
HKUST CHEM (UG)
UW HACKERFAB UWASIC
ABRAAR
TMU CE (UG)
LCRAIN
VICTORIA
UW NE (UG)
IQC URA
UWASIC
ASHMITA
UCD ECE
(PG)
REZA
UCD ECE
(PG)
NITIN
UCSB EE (PG)
MEDIATEK
AMS DESIGN ENGINEER
BELKACEM
UT EE (PHD)
AUTOMATION LAB
OUR TEAM
THANK
YOU
PROJECT INFO